AMERICAN CAR CRAFT INSTRUCTIONS

2010 CAMARO LS3 CUSTOM PLENUM SHROUD COVER

#103034 #103035

Parts Included

4x   ¼” 20 Clip Nuts

4x   Flat Head Bolts

4x   Tight Stainless Washers

4x    Yellow spacers

Illuminated Versions Only Below

1x   Red and Black 5amp Fused Wire Harness

4x  Zip ties

Introduction: This new and unique accessory has been designed to expose the factory plenum cover allowing you to paint the factory plenum or chrome plate it for an even more custom look.

Liner Information:  Your new accessories will come to you with a protective surface liner. Leave this liner in place until the installation is complete to prevent finger prints and or possible scratches during installation.

In order to install this part you will need to follow the engine wire tuck procedures on the following page. This will explain how to rearrange a few things so that you will have a nice neat engine set up prior to this installation.

1. With the engine wire tuck procedures completed the first step will be to install the Four 1/4 20 clip nuts provided in your kit directly to the newly exposed tabs protruding from each of the two fuel rails. Set the clips in place so that the threaded sleeve of the clip nut faces inward toward the plenum.

2. You have been provided with four flat headed bolts and four tight stainless washers. Place each of the bolts through a washer. Set the new shroud over the fuel rails and align the holes. This may require you to slide the clip nuts around a little until you get correct alignment. It is important to know that the new shroud has been designed to not touch the plenum leaving a varying space all around the part. Should you elect to paint the factory plenum cover; this space will serve you well in not damaging the plenum while allowing lighting to shine up through if you chose to install the lighted version of this new shroud. Although it should not be necessary to adjust the shape or angle of the new plenums sides, we have supplied some spacers to allow you to set the new shroud to the fuel rails without warping and or changing this angle. Simply set the new shroud in place to determine if spacers are needed, if any at all.

3. Once you have achieved a nice alignment and everything looks to be nice and even simply install the bolts.

TECH INFO; the tight stainless washers need only be used if you are also installing the ACC custom fuel rail covers. This washer is provided to create a space for the fuel rail cover to slide onto. If you are not installing these parts at this time do not use the washers and simply snug the bolts after removing the protective liner.

4. If your new shroud is an illuminated version you will been provided with a single red and black fused wire harness. Prior to installing the new shroud simply route this harness up to the engine plenum and secure it with the zip ties provided. The electrical connection should be routed toward the heavy red battery jump post. This will require you to obtain a switch and additional electrical connectors that will allow you to place the switch at your desired location.

American Car Craft LLC

18924 Sakera Rd Hudson, FL. 34667

Ph 727.861.1500     Fax 727.861.1520

www.americancarcraft.com