AMERICAN CAR CRAFT

18924 SAKERA RD HUDSON FL  34667

Phone: 727 861-1500               Fax: 727 861-1520

www.americancarcraft.com

INSTALLATION INSTRUCTIONS FOR THE

CHROME CAP COVERS

PARTS INCLUDED:

___ Chrome Cap Cover/Covers

___ 1-Adhesive Promoter Pack

These new and unique caps are designed to set over the factory cap as a cosmetic cover only. These chrome plated steel caps are simple to attach and offer a nice clean look.

1. The first step for installation will be to thoroughly scrub the top of the factory cap with alcohol to remove any surface contaminants then swipe the top with the adhesive promoter provided.

2. You have been provided with 2'' furry Velcro attachment cookies on the underside of the cap. Peel the release liner from the back of the cookie and firmly set them to the top of the factory cap.

3. Simply set them in place.

4. Repeat process for each cap if you have purchased more then one.