AMERICAN CAR CRAFT

18701 Old Shady Hill Rd. Spring Hill, Fl. 34610

Phone: 727 857-1151               Fax: 727 856-0273

www.americancarcraft.com

HHR STAINLESS 3PC UPPER HOOD CAP

INSTALLATION INSTRUCTIONS

PART # HHUH101

PARTS INCLUDED:

___3-Stainless Plates

___1-Adhesive Promoter Packet

Your new inserts come to you with a clear protective liner. Do not remove this liner until installation is complete.

Your new inserts have been designed to fit into the upper hood catch as well as the two key hole shaped recesses to offer a nicely finished upper hood area.

- Remove the two center redundant hood stops. NOTE: These will not be reused. Prepare the three areas first by scrubbing with rubbing alcohol to remove any road grime and dirt then swipe the areas once with the adhesive promoter provided.

- You will notice that the two smaller keyhole shaped inserts have an attachment tape applied to the back of the part. This tape is not sufficient to permanently install these parts and must be used in unison with clear 100% silicone applies to the part prior to install. Simply apply a golf ball sized blob to the back of the insert then remove the red release liner from the inserts and set in place.

- The center insert installs without silicone. Simply peel the release liner from the back of the insert and set in place. Peel the protective liner.

If any questions occur during installation, please contact American Car Craft at 727 857-1151. Thank you and enjoy your new purchase.

Note: Care must be taken when cleaning your covers. It is a good idea to lightly dust your covers with a clean soft cloth first in order to prevent any particles from scratching them. Then wipe (using a new clean soft cloth) with a good quality streak free glass cleaner.