AMERICAN CAR CRAFT

18701 Old Shady Hill Rd. Spring Hill, Fl. 34610

Phone: 727 857-1151               Fax: 727 856-0273

www.americancarcraft.com

HHR STAINLESS WIPER COWL COVER

INSTALLATION INSTRUCTIONS

PART # HHWC125

PARTS INCLUDED:

___1-Stainless Wiper Cowl Cover

___4-Zip Ties

___1-Adhesive Promoter Pack

You new cover comes to you with a clear protective liner. Do not remove liner until instructed.

Your new insert will set directly into the outlined curved section of the factory wiper cowl.

1. Remove the five harness retainers protruding through the top and face of the factory wiper cowl. Reattach this harness along the back of the engine to the other harness there with the four zip ties provided.

2. Scrub the top of the factory cowl with alcohol to remove dirt. Then swipe the area with the adhesive promoter provided. Before permanently installing, place the insert into position to check the fit and also to get acquainted with just how it will set in place. Once you have got a good idea about how you will set the insert simply remove the red release liner from the back of the cover and set in place. Press firmly along its length to set. Remove the protective liner.

If any questions occur during installation, please contact American Car Craft at 727 857-1151. Thank you and enjoy your new purchase.

Note: Care must be taken when cleaning your cover. It is a good idea to lightly dust your cover with a clean soft cloth first in order to prevent any particles from scratching it. Then wipe (using a new clean soft cloth) with a good quality streak free glass cleaner.